Networking course free code camp: (preparing to configure, manage and troubleshoot network).

Preliminary info:

A network is a collection of computers, servers, mainframes, network devices, peripherals, or other devices connected to one another to allow the sharing of data.
Network nodes:
nodes are connection points, redistribution points or otherwise end points
They are generally programmed to identify, process and transmit data from one node to another

a node is nothing but a computer or another device like a printer, Each node has an exclusive address for a network like a DCL (data link Control) or Mac (media Access control)

Types of network nodes:

internet networks:
In internetworks, host computers are physicial nodes that are recognised with the help of an IP (internet protocol) address.
Some data link equipment such as WLAN access points do not inculde IP host addresses.
These are considered LAN nodes or physical network rather than hosts or internet nodes.

Data Communications:
physical network notes in data communications include mainly data communicating equipment. They are arranged between DTE (data terminal equipment) n as well as data transmissions circuits. These devices include bridges, switche,s, hubs otherwise modems. The main function of these devices is to perform coding, signal conversions and line lock

LAN:
Short for Local area network. A lan has ntworking equipement or computers in close proximity to each other, capable of communicating, sharing resources and information. Most home and buisiness networks or on a LAN

Cache
it is a data storing technique that provides the ability to access data or files at a higher speed.
Cache’s are implemented both in hardware and in software
.Caching serves as an intermediary component between the primary storage and the recipient hardware or software device.

In its hardware form it is a small form factor of internal memory that stores instances of the most frequently executed programs in the main memory to enable faster access when they are requested by the CPU.

A very common ex of caching is in a web browser, where a website HTML, images, javascript and CSS is cached locally so that a page will loaded faster after its first hit.

DNS (Domain Name system)
it converts human readable domain names (like www.google.com) into internet Protocl (IP) addresses (like 173.194.39.78
Computers only communicate using serires of numbers so DNS was developed as a sortof “Phone book” that translates the domain you enter into your browser into a computer readable Ips.
The domain names and respective IP addresses or stored on “nameservers”. They are located all over the world.

Default gateway in networking
(a gateway can be thought as an intermediate device between the local network and the internet)
It makes it possibel for devices in one network to communicate with devices of another network.

The Open systems Interconnection (OSI) model was developed as a way to help disparate computing systems communicate with each other.

It is composed of 7 layers:

Layer 1 Physical
Layer 2 Data Link
Layer 3 Network
Layer 4 Transport
Later 5 Session
Layer 6 Presentation
Layer 7 Applications

Network devices intro:

Layer 1 devices

Analogue modems:
the word modem is a contraction of modulator/demodulator
They were developed to take signals coming froma digital node and covert it to an analog signal (hence modulating the signal) to be placed on the wire.
It would in return accept an analog signal from the wire and convert it to a digital signal that the node could understand.
They were developed to create connections between network segments via public switched telephone network (PSTN) using the plain old telephone system (POTS)
Modems provide for a single connection to a networks

Hubs:
A hub is a repeater: it does not care where the signal is coming from or where it is going. It just takes the electrical signal that arrives on the port and replicates the signal out all the other ports.
A hub may have just a few ports or many ports.
It does not have an IP, and it is used to connect multiple computers and network devices together.

Layer 2 devices:

Switches
A switch utilizes an application specific integrated circuit (ASIC) chip
This chip is programmed to let the switch learn when a device is on a network and which ports it is connected to via the device’s layer 2 mac address. (this is what it makes it a layer 2 device).
A switch can only communicate with the local network devices.
It is a hardware device that filters and forwards network packets

Wireless Access point (WAP)
A WAP is a specific type of network bridge that connects (bridges) wireless network segments with wired network segments.
A WAP will only communicate with local network devices

Layer 3 devices:

Multilayer Switch (MLS)
A MLS will provide normal layer 2 network switching services but it will provide also Layer 3 or higher OSI model services.
Most commonly it will function as a layer 3 switch.

It not only has an ASIC chip for switching but that chip is also programmed to handle routing functions . This allows the device to communicate and pass data to non local network devices.

MSL are highly programmable and cancan have just a few ports or many ports.

Router:
A router is a device for connecting different networks together using the OSI model’s layer 3 logical information.
It uses software programming for decision making as compared to the switch’s use of an ASIC chip.
The router uses this programming to keep track of different network and what consideres to be the best possivble route to those network.

It can communicate with both local and non local network devices.
It is designed to receive, analyse and move incoming packtets to another network

Layer 4 devices: (mostly security devices and optimization and performance devices)

Security devices)

firewalls:
Firewalls can be placed on routers or hosts, or they can be their own device.
They function on multiple layers of the Osi model (specifically layers 2,3 4, and 7)

Their purpose is to block packets from entering or leaving the network.
(they are like a police officer of the network). They can inspect packets in two ways:

Via stateless inspection
They will examine every packet against a set of rules. Once a packet matches a rule, the rule is enforced and the specified action is taken.

Via stateful inspection
The firewall will only examine the state of the connection between networks.
Specifically when a connectio is made from an internal network to an external network the firewall will not examine any packets returning from the external connection.
As a general rule, external connections are not allowed to be initiate with the internal network.

A firewall is a the first line of defense in protecting the internal network from outside threats.

Intrusion detection system (IDS)
And IDS is a passive system designed to identify when a network breach or attack against the network is occurring.
It is usually designed to inform the network administrator when a breach attack has ocurredd through log files, sms and or email notification.
They cannot prevent or stop a breach from happening on tehir won
It recievs a copy of all traffic and evaluates it against a set of standards.:

signature based: evaluates network traffic for known malware or attack signatures
anomaly based: evaluates network traffic for suspicious changes
policy based: evaluates network traffic against a specifically declared policy

Intrusion prevention system (IPS)
An active system designed to stop a breach or attack from succeeding in damaging the network.
Designed to perform actions that stop malicious activity.
Will inform the administrator through the use of a log files, sms or email notification

All traffic on the network segment flows throguh the IPS to either enter or leave the segment.
Like the IDS all traffic is evaluated against a set of standards.

It is usually placed between a router (with a firewall) and the destination network segment.
It is programmed to make an active response to the sitiuation:
-Block the offending IP address
-close down the vulnerable interface
-terminate the work session
-redirect the attack
-and more

VPN Concetrator
 It is a type of router device built specifically for managing VPN communication infrastructures.
It will allowe for many more secure VPN connections to a network
It’s a type of networking device that secures creation of VPN connections and delivery of messages between Vpn nodes.
It has the ability to create and manage a large quantity of VPN tunnels.

Furtherrmore it can:
-establish and configure tunnels
-authenticate users
-assign tunnel?ip addresses to users
-encrypt and decrypt data
-ensure end to end delivery of data

Most concentrators can function on layer 2,3,7 of the OSI model, providing Ipsec encryption through a secure tunnel.

Optimisation and performance devices

Load Balancer
(aka content switch or content filter)
Used to to loead balance between multiple hosts that contain the same data, spreading out the workload and efficienty.

It is commonly used to distribute the requests (workload) to a server farm among the various servers, helping to ensure that no server gets overloaded.

Proxy server:
It is an appliance that requests resources on behalf of client machine.

Often used to retrieve resources from outside untrusted networks on behalf of the requesting client.
It thus hides and requests the requesting client.

It can also be utlised to filter allowed content.

It can increase network performance by caching commonly used web pages,

Networking services and applications (the basics of a VPN and the protocols used by a VPN)

VPN basics: what are they?

(viritual private netwrok ) used by remote hosts to access a private network through an encrypted tunnel through a public network.

Once the connection is made, the remote host is no longer considered remote. It is seen by the private network as a local host.
Even if though the network traffic may pass through different routers or systems, it is seen by both ends as a direct connection.

VPNs can help reduce networking costs for organisations and buisinesses. This is partly achieved ebcause the VPN does not require the use of a dedicated leased line to create the connection.

VPN types:
-site to site VPN = allows a remote site’s network to connect to connect to the main site’s network	and be seen as a local network segment (vpn concentrators on both ends of	the VPN will manage the connection) .
companies with offices in multiple fixed locations to create secure	connections between each other over the internet.
-remote access VPN (host to site VPN) = allows select remote users to connect to the local network.	A VPN concentrator on the local network will manage the connections	coming from remote users. (commercial vpns, enable to bypass regional	blocks)
The remote system making the connection uses a special software, called	VPN client software to make the connection.
-host to host VPN (SSL VPN)= allows a secure connection between two systems without the use of	the VPN client software. A VPN concentrator on the local network	manages the connections.
    The host seeking to connect uses a web browser that supports the	correct encryption technology (either SSL or TLS) to make the	connection to the VPN concentrator. To gain access to the safe	connection, the software needs to be launched and authenticated	with VPN username and password This is how the encrypted link	is built between the device and the remote network for secure	exchange of data.

Internet Protocol Security (IPSec)
The most common suite of protocols to secure a VPN connection.
It works at layer 3 of the OSI and above.

Can be used with the authentication header (AH) protocol. This protocl only offers authentication services, no encryption.

It can also be used with the encapsulating security Payload (ESP) that both authenticates and encrypts packets.

Both AH and ESP will operate in one of two modes:
1) transport mode: between two endpoints ( eg as in the host to host VPN)
2)tunnel mode: between two endpoints ( site to site VPN)

IPSec implements Internet security association and key management (ISAKMP): a method for transferring security key and authentication data between systems outside of the security key generating process

Generic routing Encapsulation (GRE)
 A tunnelling protocol that can encapsulate a variety of network layer protocols.
Often used to create a sub tunnel within an Ipsec connetion.

This is because Ipsec will only transmit unicast packets (one to one connections), but often there is a need to transmit multicast or broadcast (one to many communication) packets across an IPSec connection.
By using GRE this is accomplished.

Point to point tunnelling protocol
 An older VPN technology that supports dial up VPN connections. Not very secure on its own, but microsoft added Gre to it making it more secure.

Transport Layer security protocol (TLS)
-cryptographic protocol used to create secure encrypted connections between two end devices or applications.
- Asymmetric encryption to authenticate end points and then negotiate a symmetrical security key that is used to encrypt the session.
-It has replaced the secure socket layer (SSL) protocol
-works at layer 5 and above of the OSI model
-All modern web browsers support TLS

Secure socket Layer (SSL) protocol
-an older cryprographic protocol similar to TLS
-commonly used in internet transactions. All web browser support SSL

Network services and applications part 2: Network access services and applications

Network access Services:

Network interface controller (NIC)
-Piece of hardware, aka Network interface card
-how a device connects to a network
-works at layers 1 and 2 of the OSI.
-At Layer 2 (data link): prbvides the functional means of entwokr communication by determining which networking protocls (ie ethernet, point to point protocl) will be used.
It also provides the local network node address through its burned in physical MAC address.
-At Layer 1 it determines how the network data trafic will be converted a bit at a time into an electrical signal that can transvers the network media being used.
Most modern computers come in with a NIC

Radius (remote authentication Dial in User Service)
-a remote access service used to authenticate remote users and grant them access to authorised network services.
- a popular Authentication, authorization and accoutning (AAA) protocol used to help ensure that only authenticate end users are using network resources they are authorised to use.
-the accounting features are very robust but its weakness is that only the requestors (end users) password is encrypted. The rest is all in plain text

Tacacs+ ( Terminal Access controller Access -control system Plus)
 A remote access service that is used to authenticate remote devices and grant them access to authorized network resources.
- Also a popular AAA protocol.
-The accounting features are not as robust as the one of the RADIUS but all transmissions between devices are encrypted.

Other Services and Applications

RAS (remote access Services)
 not a protocol but a roadmap.: a descritpion of the combination of software and hardware required for remote access connection.
A client requests access from a Ras server which either grants or rejects access.

Web services
Provides means for communication between software packages or disparate platform. Usually achieved by translating communication into an XML (extensible Markup Languae) format

Unified Voice Services
 A combination of software and hardware required to integrate voice communications and channels into a network

DHCP in the network

Static vs dynamic IP addressing

How does a computer know what its IP configuration is?
Most likely a computer received its IP configuration from a DHCP (dynamic Host configuration Protocol) server.
The server gave the computer an IP address and told it where its default gateway as, as well as how to find a DNS server.

Static IP addressing:
 the admin assigns an ip number and subnet mask to each host in the network,
Each network interface that is going to be available to connect to the network requires this information.

The admin assigns a default gateway location and DNS server location to each host in the network.

Each time a change is made (eg a new default gateway is established) each IP configuration on each host must be updated.

Dynamic IP addressing:
the admin configures a DHCP server to handle the assigning process, which automates the process
- the dhcp server listens to a specific port for IP information requests.

Once it recieves a request, the server responds with the required information.

Typical DHCP process

upon boot up, a PC that is configured to request an IP configuration sends a DHCP discovery packet.

- The discovery packet is sent to the broadcast address: 255.255.255.255:67 (port 67)
- the dhcp server responds with an offer packet (I am here to help)
- the offer packet is sent to the MAC address of the computer using UDP port 68
-the computer recieves the offer packet from the DHCP server and returns a request packet (requesting the proper IP configuration) to the DHCP server.

-Once the DHCP server recieves the request packet, it sends back an acknowledgment packet which contains the required IP configuration.

Upon reciept of the acknowledgment packet, the PC changes its IP configuration to reflect the information received.

Components and processes of DHCP
Ports used:
PC sends discovery packet to 255.255.255:255:67
DHCP sends offer packet to the PC’s MAC (media access control address) address on port 68

address scope
 the ip address range that the admin can hand out.
 admin configures Ip address range with one that is available to be handed out.

Address reservations
 the admin reserves specific Ip addresses to be handed out to specific MAC addresses. These are used for devices that should always have the same Ip address (eg servers, and routers)
-it allows for these addresses to be changed from a central location instead of having to log into each device separately.

Leases
- configuration parameters are only good for a specified amount of time.
-Leases are configured by the administrator
(time limit for which an certain IP configurations is valid

Options (various options the admin can configure)
default gateway locations
-DNS server addresses (there can be more than one)
- time server addresses (PC can syncrhonise with a time server)
- many additional options

preferred Ip configuration
- a PC can have a preferred IP addresses. (ie the ip it had the last time it booted up)
-the admin can configure DHCp server to either honor the preference or ignore it.

Under the right circumstances a DHCP server isn’t requried to reside on the local network segment.
Broadcast transmissions cannot pass throguh a router. If there is no DHCP server on the LAN, the router can be configured to be a DHCP relay (Ip helper). Whne it recievs a discovery packet from a node, it will forward that packet to the network segment on which the DHCP server recsides.

This allows for fewer configured DHCp servers in anny given network, reducing the ammount of maintanance an admin needs to perform.

Introduction to the DNS service

DNS is the process that maps human friendly names to IP addreses. Without that we would have to memorize Ip addresses. It’s like the phone book of the internet.

DNS stands for domain name system, and is very hierarchical in nature. If the local DNS server apparatus does not contain the needed record, it sends a request up the chain until a positive response is received, which gets passed back down to the original requestor.
DNS requires a FQDN (fully qualified domain name) in order to function. Fqdn = www.google.com

Www = the specified services
google. = the local domain
com = the top level domain: contains the google, contains the services

 Different levels of DNS servers:
-local dns server the server on the LAN that contains the HOSTS file that maps the FQDn to IP addresses in the subdomain
-Top level domain (tld) server: the server that contains the records for a top level domain
examples include: .com, .org, .net, .edu
each of these servers contain all the information for their respective domains
-TLD servers delegate down to second level servers to ease the load, however the TLD	server is the responsible server

 root server: the server that contains the records for the TLD servers

authortitative:
 - an authoritative dns server is the one that responds to a request that has been specifically	configured to contain the information
- an authoritative response comes from the DNS server that actually holds the original record

 non-authoritative:
- a non authortitative dns server responds to a request with DNS information that it received from another DNS server
- a non authoritative response is not a response from the official name server for the domain.
Instead, it is a second or third hand response (or even further removed)

 DNS records

-A record: maps hostnames to their IPv4 addresses
-AAAA record: maps hostnames to their IPv6 addresses
-CNAME record: maps canonical (alias) names to hostnames
-PTR record: pointer record that points to a canonical name
- MX record: maps to the email server that is specified for a specific domain. It is the record that determines how email travels from sender to recipient.

 Dynamic DNS (DDNS)
 -permits lightweight and immediate updates to a local Dns database
-very useful when FQDN remains the same but the Ip addresses is able to change on a regular absis.
- is implemented as an additional service to dns

DDNS updating
- a method for updating traditional name servers without the intervention of an administrator
- a DDNS provider supplies software that will monitor the Ip address of a referenced system. Once the Ip addresses change, the software sends an update to the proper DNS server

- DDNS is useful when access is needed to a domain whose Ip addresses is being supplied dynamically by an internet service Provider (ISP)

 Introducing Network address translation

Network address translation (NAT) solves the problem of how to route non routable IP addresses.

In an effort to conserver the Ipv4 address space, the rpovate IPV4 addressing spaces were introduced. These address spaces were removed from the public IPv4 address spaces and made non routable across public IPv4 networks.

This prevented private IPv4 addresses from communicating with remote public networks.
Nat very simply solves this problem: a router with NAT enabled will translate a private Ip address into a routable public IP address. When the response returns to the router, it passes the response back to the device that requested it.

This is just like how multiple people living in one house all have the same address for mail to be sent to. Once a parcel arrives at the doorstep, the people inside the house decide amongst themselves for which person the parcel was for.

 How network address translation works:

There are two categories of Nat:
- static NAT: each private IP address is assigned to a specific routable public Ip address. This relationship is kept and maintained by the Nat enabled router.

-when a device access outside of the LAN the router translates the local Ip address to the assigned public Ip address. When the response come back, the router will translate the public IP address into the local one.

 Dynamic Nat (DNAT)
 The NAT enabled router dynamically assigns a routable IP address to devices from a pool of available public IP addresses,

-When a device needs access outside of the LAN, the router performs the NAT function, only the public IP address comes from a reusable pool of public Ip addresses. When a device has finished accessing the outside network, the public IP address goes back into the pool

- as initially designed the DNAT was more flexible than SNAT but still led to some scalability issues. As more network traffic requires access to remote networks, the pool of available public Ip addresses needs to increase or outside access cannot be achieved

Port address translation (PAT)
-PAT is a type of DNAT that was developed to increase scalability of PAT.
-When a LAN service requires access to a public network, the NAT enabled router dynamically assigns the public IP address to the device with the addition of dynamically assigning a port number to the end of the public IP address.

-The router tracks the Ip addresses and port nunbers to ensure that the network traffic is routed to and from the proper services.

-PAT still requries a pool of Public Ip addresses but the pool may only contain one address or it may contain several for a large private network

-This is the preferred method for implementing NAT for two reasons: less public IP addresses are required and it is also easier for admins to maintain.

 The NAT terminology

- inside local address: a private IP address on the LAN. The Up address assigned to a specific	device.

- inside global address: a public Ip address referencing an inside device. The public IP address	assigned to the inside device by the NAT enabled router to allow access	outside the public network.

-outside global address: a public Ip address referencing to an outside device. The public address	assigned to a device outside a LAN

-Outside local address: a private Ip address assigned to an outside device. The private address	assigned to an outside device on the interior of the LAN

What makes a WAN a WAN (wide area network) as opposed to a LAN

 If you are using a form of transmission that you don’t own, (eg you are leasing it or paying it) then you are most likely using wan technology.

One of the most common physical infrastructures used in WAN technology is the public switched telephone network due to its widespread availability (PSTN).

Wan technologies:

- dial Up : it utilises PTSN to transmit network traffic as an analog signal. Requires an analog	modem to format the network traffic.

ISDN (integrated services digital network)

 -Digital point to point Wan technology using the PSTN
- completely digital services
- requires the use of a terminal adapter (TA) for the connection to the end node (often called a digital modem).
-A primary rate interface (PRI) uses 23 64kbs B channels and one 64kbps D channel for call setup and link management.

achieves 1.544 mbps speed (T1 leased line)
- Commonly implemented as a Basic rate interface BRI using two B channels and one D channel.
-Achieves 128kbps speed.

Not as capable as DSL (digital subscriber line) but it can often be implemented where the DSL cannot be installed.

  Publcic Switched telephone network:

 -XDSL a digital WAN technology using the PSTN
-requires the use of a digital modem
dedicated digital line between the end point and a class5 central office (CO)
- it is only possible within 18,000 feet of the CO
-carries voice and data (filters are put in place to get voice)

 SDSL (symmetric DSL)
- synchronous in nature (upload and download speed is the same)
-does not carry voice communications
-if voice is required, an additional line is needed.
- used by buisiness that don’t need the performance of a t-1 leased line, but that do require the symmetrical upload and download speeds.

ADSL (asymmetric DSL)
- async in nature (upload speed is slower than download speed)
- can carry data and voice
- most common implementation of DSL in the SOHO (small office/ home office) environment.

VDSL (very high bit rate DSL)
- async in nature
-used in high quality video and VoIP necessary
- it is only possible when located within 4, 000 feet of a CO),
-Current standard allows for up to 100mbps over PTSN
- to achieve that, the end point must be within 300 meters of a CO (central office)

 Broadband cable

-Coaxial cable networking
-broadband connection to a location delivered by the cable company
-it can deliver voice, data and television all through the same connection
-headend: all cable signals are received at this point; signals are processed and formatted then transmitted back to the distribution network.

 Distribution network: smaller service areas served by the cable company. The distribution network architecture can be composed of fiver optic cabling, coaxial cabling and/or hybrid fiber coaxial cabling HFC
-Unlike DSL, the bandwith is shared by the distribution network, this can lead to the increased latency and congestion.

-Final distribution to the premise is usually through a coaxial cable.

-data over cable service interface specification DOCSIS the specifications for how the signal will be received. All cable modems and similar devices must measure up to the ISP’s required DOCSIS standard.

Fiber optic networking
 -uses light to transmit data and voice
-allows or more bandwith over greater distances.
-more expensive to install, but less susceptible to noise.
--dense wavelength division multiplexing (DWDM) is a method of multiplexing several Optical carrier levels (up to 32 channels) into a single optical fibre, effectively increasing the bandwith of a single optical fibre.

- Coarse wavelenght division multiplexing (CWDM) is similar to DWDM but only allows for up to 8 channels on a single fiber.

-Passive optical network (PON) is point to point technology that uses a single optical fiber to connect multiple locations to the internet.
It uses unpowered optical splitters.

Cellular networking
-cellular networking involves using the cellular phone for more than just phone calls
1G cellular was only capable of voice transmissions
-2G cellular added simple data transmission capability (text)
-2 EDGE offered some basic cellular networking connectivity
-3G is the beginning of broadband WAN networking
-4g consists of LTE (long term evolution)+hspa (high speed packet address)

 Wimax WAN connections

 Stands for World wide Interoperability for microwave networking
-originally developed as an alternative use when DSL or cable was not available.
-uses microwave transmissions as an over the air method to transmit voice and data
-requires a site of line between relay stations

- It is compatible with LTE networks but not compatible with 3G networks

 Satellite WAN connections
-uses microwave transmissions
-useful for extending networks to places that are hard to reach
-microwave relay is a method of transmitting through the atmosphere
-requires line of site between relay stations
- a communication satellite (comsat) orms part of the microwave relay networking

WAN technologies part 3

Metro ethernet wan connections
- when a service provider connects to the customer’s site through an RJ45 connector
the customer views the WAN connection as an ethernet connection while in reality the type of connection will be dependant on the level of surface that has been purchased:

 Leased Line WAN connections

A dedicated circuit (connection) between two endpoints used for communications
- it can utilise either a plain old telephone service line on the public switched telephone network or it can be a fiber optic provided by a telecommunications company

-it is usually a digital point to point connection
-the circuit cannot be used by any other entity other than the customer.
- the speed of the line is limited by what the customer is willing to pay.

 An important leased line connection is the Point-to-point Protocl (PPP) , a common data link

-layer (OSI layer2) protocol used with leased line networks
-It can transmit multiple layer 3 protocols (IP and IPX) through the use of control protocols
it also includes a feature called multilink PPP which allows for multiple physical interfaces to be bonded together and act as a single logical interface, effectively increasing the available bandwith